## Slide 1: Crystallography with an FEL
Marc Messerschmidt
BioXFEL Science and Technology Center
Buffalo, June 2014

## Slide 2: Outline
The LCLS
  Machine capabilities
  Spectrum
LCLS instruments for crystallography
CSPad detector
sample injectors for serial femtosecond crystallography
First results
Future Developments

## Slide 3: Linac Coherent Light Source
San Francisco
SLAC

## Slide 4: LCLS Performance
32 undulators
  Total length: 132 m
Spectral coverage: 0.3-10.5 keV
  3rd harmonic to 25 keV
    up to 1% of fundamental intensity
up to 1013 photons per pulse
0.01 - 3% bandwidth (0.3% jitter)
Pulse duration: 3-500 fs
Repetition rate: 120 Hz
P. Emma, et al., Nature Photonics, 4(2010), 641-647

## Slide 5: LCLS initial performance
First lasing and operation of an angstrom-wavelength free-electron laser
Author(s): Emma, P (Emma, P.)[ 1 ] ; Akre, R (Akre, R.)[ 1 ] ; Arthur, J (Arthur, J.)[ 1 ] ; Bionta, R (Bionta, R.)[ 2 ] ; Bostedt, C (Bostedt, C.)[ 1 ] ; Bozek, J (Bozek, J.)[ 1 ] ; Brachmann, A (Brachmann, A.)[ 1 ] ; Bucksbaum, P (Bucksbaum, P.)[ 1 ] ; Coffee, R (Coffee, R.)[ 1 ] ; Decker, FJ (Decker, F. -J.)[ 1 ] ; Ding, Y (Ding, Y.)[ 1 ] ; Dowell, D (Dowell, D.)[ 1 ] ; Edstrom, S (Edstrom, S.)[ 1 ] ; Fisher, A (Fisher, A.)[ 1 ] ; Frisch, J (Frisch, J.)[ 1 ] ; Gilevich, S (Gilevich, S.)[ 1 ] ; Hastings, J (Hastings, J.)[ 1 ] ; Hays, G (Hays, G.)[ 1 ] ; Hering, P (Hering, Ph.)[ 1 ] ; Huang, Z (Huang, Z.)[ 1 ] ; Iverson, R (Iverson, R.)[ 1 ] ; Loos, H (Loos, H.)[ 1 ] ; Messerschmidt, M (Messerschmidt, M.)[ 1 ] ; Miahnahri, A (Miahnahri, A.)[ 1 ] ; Moeller, S (Moeller, S.)[ 1 ] ; Nuhn, HD (Nuhn, H. -D.)[ 1 ] ; Pile, G (Pile, G.)[ 3 ] ; Ratner, D (Ratner, D.)[ 1 ] ; Rzepiela, J (Rzepiela, J.)[ 1 ] ; Schultz, D (Schultz, D.)[ 1 ] ; Smith, T (Smith, T.)[ 1 ] ; Stefan, P (Stefan, P.)[ 1 ] ; Tompkins, H (Tompkins, H.)[ 1 ] ; Turner, J (Turner, J.)[ 1 ] ; Welch, J (Welch, J.)[ 1 ] ; White, W (White, W.)[ 1 ] ; Wu, J (Wu, J.)[ 1 ] ; Yocky, G (Yocky, G.)[ 1 ] ; Galayda, J (Galayda, J.)[ 1 ]
Source: NATURE PHOTONICS Volume: 4 Issue: 9 Pages: 641-647 DOI: 10.1038/NPHOTON.2010.176 Published: SEP 2010
Times Cited: 563

## Slide 6: Hard X-ray spectrum at LCLS

## Slide 7: AMO instrument
Atomic, Molecular and Optical Science
with ultrafast and ultraintense X-rays at the LCLS
Techniques
Electron time-of-flight spectroscopy
Ion time-of-flight spectroscopy
Ion imaging
Ion momentum spectroscopy
X-ray scattering

## Slide 8: Femtosecond Protein Nanocrystallography Using Soft X-rays
Low resolution structure of Photosystem I determined from ~15,000 nanocrystals
Each crystal was illuminated sequentially and destroyed by the LCLS beam
Dose ~30 times larger than classical damage limit
  >700 MGy
Unfortunately, low photon energy at AMO limited resolution and chance for new biology
Synchroton
LCLS
Chapman et al. Nature Physics 470, 73-77 (2011)

## Slide 9: XPP instrument
Scientific Applications
Femtosecond Structural Dynamics
X-ray Interactions with Matter
X-ray Techniques
Wide Angle X-ray Scattering/Diffraction
Small Angle X-rays Scattering
X-ray Absorption Spectroscopy
X-ray Emission Spectroscopy

## Slide 10: XPP instrument

## Slide 11: Coherent X-ray Imaging Instrument

## Slide 12: CXI Layout
Diagnostics &
Wavefront Monitor
1 micron Sample Environment
1 micron KB
(inside thermal enclosure)
Diagnostics/Slits
0.1 micron KB & Sample Environment
Particle Injector and Ion TOF
Refocusing Lenses
Boutet & Williams, New Journal of Physics 12, 035024 (2010)

## Slide 13: Cornell-SLAC Pixel Array Detector (CSPAD)
Cornell-SLAC Pixel Array Detector
2D Pixel Array Detector
  High resistivity Silicon (500 µm) for direct x-ray conversion.
  Reverse biased for full depletion.
  Bump-bonding connection to CMOS ASIC.
<1 photon readout noise
110x110 µm2 pixels
1516 x1516 pixels
>103 dynamic range
120 Hz readout
Tiled detector, permits variable ‘hole’ size
Collaboration with the Gruner Group at Cornell University

## Slide 14: High Resolution Structure of Lysozyme Obtained Using Serial Crystallography
Dose is greatly reduced with 9 keV compared to 2 keV
~30 MGy or less with 3 micron focus and 1 x 1 x 3 micron crystals
Boutet et al., High-resolution protein structure determination by serial femtosecond crystallography. Science , 337(6092):362–364, 2012.

## Slide 15: Lysozyme Bragg peaks are observed to the edge of the detector
Lysozyme single-shot diffraction at 9.3 keV, 40 fs pulses
Peaks observed to corner of the detector
  < 2 Å resolution
Resolution limited by photon energy and experimental geometry
1.86 Å resolution in the corner
Boutet et al., High-resolution protein structure determination by serial femtosecond crystallography. Science , 337(6092):362–364, 2012.

## Slide 16: Liquid Jet Development at ASU
Many years of development by ASU at the ALS to optimize the system
Liquid jet for LCLS uses gas focusing
  Prevents clogging
  Submicron droplets from a bigger nozzle
Jet velocity
  ~10 m/s
Jet diameter
  ~4 micron
U. Weierstall, J. C. H. Spence, and R. B. Doak
Rev. Sci. Instrum. 83, 035108 (2012)

## Slide 17: LCP stream hit by XFEL beam
X-ray pulses
green laser illumination synchronized with the LCLS X-ray pulses at 120 Hz
100μm
1.6 mm/sec (190 nL/min)
LCLS at 120Hz
50 μm jet

## Slide 18: Electrokinetic Injection for PCS at CXI: MESH on a Stick
Low flowrates (100’s nl/min)
  Viscous media slows flow
  Crystal-friendly additives such as glycerol, sucrose, and PEGs
Filter- and union-less setup
  Continuous capillary from reservoir to tip (ID: 50 – 100 µm), 1.5 m long
Carrier fluid should contain ions (~100 mM) and a viscous additive (e.g. 30% glycerol)
  Common to most cryo-protectant mother liquors
Applied voltages ~3 kV
Contact Ray Sierra from PULSE
6 mm

## Slide 19: Structure determination of TbCatB by molecular replacement reveals a complex with a pro-peptide at 1.9 Å
Koopmann etal, In vivo protein crystallization opens new routes in structural biology. Nature Methods , 9(3):259–U54, 2012
In-vivo grown crystal of a glyco-protein not previously known to high resolution
New glycan moiety
Pro-peptide bound to the active site
New glycan moiety bound to pro-peptide

## Slide 20: PCS program
http://www-ssrl.slac.stanford.edu/lcls/users/proposals.html
http://www6.slac.stanford.edu/news/2013-07-17-CRYSTAL-SCREENING-LCLS.aspx
fully supported GVDN system
only little sample needed
full data sets possible
about 4 month from deadline to running
6h beam time blocks

## Slide 21: Recent Publications
X-Ray Diffraction from Isolated and Strongly Aligned Gas-Phase Molecules with a Free-Electron Laser. Phys. Rev. Lett. 112, 083002 – (Feb 2014)
De novo protein crystal structure determination from X-ray free-electron laser data. Nature 505, 244–247 (Jan 2014)
Lipidic cubic phase injector facilitates membrane protein serial femtosecond crystallography. Nature Communications 5, Article number: 3309 (Feb 2014)
Accurate macromolecular structures using minimal measurements from X-ray free-electron lasers. Nature Methods (Mar 2014)
Femtosecond X-ray diffraction from two-dimensional protein crystals, IUCrJ (2014). 1, 95-100
... still much more to come

## Slide 22: Future perspectives
Improvements
  quick standard experiments (PCS)
  bigger and better detectors
  beam sharing
  more flexible sample handling
  easy to use analysis
New sources
  more instruments available
  higher repetition rate

## Slide 23: Creating More Beamtime at LCLS
Serial Serial Femtosecond Crystallography
The beam passing through a 4 micron water jet is minimally attenuated
> 97% transmission for 4 keV and above
Refocus and reuse the beam

## Slide 24: European XFEL

## Slide 25: European XFEL
5MHz repetition rate
  about 10x300 pulses/s for SFX station
  fast triggers necessary
  faster sample delivery
large energy range 3-25 keV
dedicated SFX experiment
  uses refocussed beam from SPB beamline
  much more beam time for crystallography

## Slide 26: Acknowledgements
BioXFEL
DOE/LCLS
DESY
CFEL
ASU
MPI Heidelberg
Cornell

## Slide 27: End of presentation